## Slide 1
V&V Results for CML Extended Planetary Derived State (delta)
Alexandre Masset
Organization (Odyssey Space Research)
Date: 12/2/2025 (version 1) – 12/2/2025 (latest)
ANTARES Artemis 2
Model V&V
Notes: 1

## Slide 2: Outline
Purpose and Use
  Assumptions and Limitations
Antares Project Status
  Location
  Associated Merge Requests and Commit Hashes
Inheritance and Dependencies
Model Inventory
Code Review
  Coding Standards Compliance
  Architecture Review
  Code Coverage
Verification / Validation Test Descriptions
Follow-on Work

## Slide 3: Model Purpose and Use
Purpose:
  Provides an extension to the JEOD PlanetaryDerivedState with additional state options to meet specific requirements. Notably, this model provides transformations and representations including Topocentric/Topodetic NED, Boost Reference, Plumbline, Launch Range, Landing Range, EI Range, Range Safety, Pad SEU and left-handed pad frames, Hang and Roll angles.
Models Using this Model:
  CML
    atmos_rel_state
    atmos_exec
    first_order_hold
    secondary_chute_atmosphere
    chute
    eg_chute
  CEV
    eg_chute
    chute_manager
    antares_extended_planetary_derived_state
  Grok
    grok_state
    grok_vehicle
    grok_main
Assumptions and Limitations
  A vector with a magnitude less than std::numeric_limits<double>::min() is zero.
  The orientation of planet depends on the models of planet and RNP in JEOD.

## Slide 4: Antares Project Status
Antares Requirements Sections E.1.2, F.1.1
Model Locations:
  cml/models/dynamics/state_descriptors/extended_planetary_derived_state
Recent Merge Requests
  !7310 (V&V)
  !6758 (JEOD to CML message)
  !4751 (point-to-point capability)
Most Recent Commit
  A.Masset, 11/04/25
  Adding subscribe pt_to_pt assert. Adding verif that pt_to_pt model can be run midsim
  53aa2d6b669856b4a1decfb8e0c33e97f6a901a0

## Slide 5: Code Inheritance and Dependencies
Code Inheritance
  JEOD PlanetaryDerivedState
Code Dependencies
  CML
    Subscriptions
    Math_utils
    Range
    CML Message
  JEOD v3.4
    planet_fixed
    ref_frames
    dyn_body
    Vector3
    Matrix3x3
    orientation

## Slide 6: Model Inventory
Documentation (docs/)
  extended_planetary_derived_state.odt
  extended_planetary_derived_state.pdf
  extended_planetary_derived_state_presentation_VV.pptx
  extended_planetary_derived_state_presentation_VV.pdf
Headers (include/)
  extended_planetary_derived_state.hh
  point_to_point.hh
  range_safety_data.hh
  topo_container.hh
  velocity_set.hh
Source code (src/)
  extended_planetary_derived_state.cc
  point_to_point.cc
  range_safety_data.cc
  topo_container.cc
  velocity_set.cc
Verification (verif/)
  SIM_ei_entry
    Log_data
                RUN_ei_entry
  SIM_planet_rel
    Log_data
                Modified_data
                ERROR_point_to_point
                FAIL_vel_set_init_NULL
                RUN_all_on
                RUN_baseline
                RUN_boost_plumbline
                RUN_boostref
                RUN_double_inits
                RUN_entry_range__common_ref
                RUN_entry_range__initial_ref
                RUN_entry_range__midsim_ref
                RUN_hangroll
                RUN_inrtl_pfix_misaligned
                RUN_landing_range
                RUN_launch_range
                RUN_plumbline
                RUN_point_to_point
                RUN_range_safety
                RUN_rel_vel
                RUN_submodels_on_midrun
                RUN_topocentric
                RUN_topocentric__with_rel_vel
                RUN_topocentric_altitude
                RUN_topocentric_topodetic
                RUN_topodetic
                RUN_topodetic__with_rel_vel
                RUN_warning_check
                common_input.py
Validation (validation/)
  None

## Slide 7: Code Review : Coding Standards Compliance
Model is compliant

## Slide 8: Code Review : Architecture Review
Class ExtendedPlanetaryDerivedState
  Main class where other objects are instantiated
  Provides several options to express the state relative to a planet
  Added subscribe_pt_to_pt()
  Added unsubscribe_pt_to_pt()
  Added is_pt_to_pt_subscribed()
  Added PointToPointManager submodel instance
Class PointToPointElement
  Gathers information (position and name) on a single point, either attached to a planet or to a vehicle
Class PointToPointPosition
  Relates two points through a relative position expressed in the planet-fixed frame
Class PointToPointManager
  Manages the list of points on the vehicle, the planet and their relative positions

## Slide 9: Code Review : Code Coverage
See exceptions in docs, Section 5.1.1

## Slide 10: Initial Project Implementation
Extensive use in many CML and CEV models
PointToPointManager added to SIM_orion
  relative_state.sm: ground_to_cm (pt_to_pt_manager)
  Not used anywhere

## Slide 11: Verification: SIM_verif
SIM_entry_ei
SIM_planet_rel
  RUN_point_to_point
  ERROR_point_to_point
  See docs, Chapter 5

## Slide 12: Follow-on Work
Documenting effect of rotations on pt_to_pt relative position
Point_to_point: Issue #2968
  Relative positions are accessed through pointers to the pt_to_pt_pos list| If multiple models access this list, and relative positions are removed: pointers are left dangling
  Using external double*[num_pts] array to log relative positions Same issue as above
FIXME: range_safety_data.hh:38
3 ToDOs: extended_planetary_derived_state.cc