## Slide 1
V&V Results for CML Vent Model (delta)
Alexandre Masset
Organization (Odyssey Space Research)
Date: 11/13/2025 (version 1) – 11/13/2025 (latest)
ANTARES Artemis 2
Model V&V
Notes: 1

## Slide 2: Outline
Purpose and Use
  Assumptions and Limitations
Antares Project Status
  Location
  Associated Merge Requests and Commit Hashes
Inheritance and Dependencies
Model Inventory
Code Review
  Coding Standards Compliance
  Architecture Review
  Code Coverage
Verification / Validation Test Descriptions
Follow-on Work

## Slide 3: Model Purpose and Use
Purpose:
  Model the forces and torques imparted by any number of vents on a dynamic body.
Models Using this Model:
  CEV
    Ammonia vent
    PSA vent
    Urine vent
Assumptions and Limitations
  Because the model is provided with a mass-derivative rate, it must use a time step to convert that derivative into a mass demand. Therefore, the discrete mass demand of a vent onto a dynamic-mass body is placed post-integration rather than pre-integration to avoid any issue with the first time step.

## Slide 4: Antares Project Status
Antares Requirements, Sections F.1.2 and F.1.4
Model Locations:
  cml/models/fhw/effectors/vent
Recent Merge Requests
  ! 7426 (V&V)
  ! 6771 (Compiler warnings cleanup)
  ! 6758 (CML Message)
  ! 6647 (CPPcheck cleanup)
  ! 5678 (CML Vents update to support new CEV vents)
Most Recent Commit Hash
  fb8705fb419535c505a4bde9f958cbd37b9805a2

## Slide 5: Code Inheritance and Dependencies
Code Inheritance
  N/A
Code Dependencies
  CML Message
  CML Subscriptions
  CML MathUtils
  CML DynamicMass
  JEOD v3.4

## Slide 6: Model Inventory
Documentation (docs/)
  vent.pdf
  vent.odt
  vent_presentation.pdf
  vent_presentation.odp
Headers (include/)
  simple_vent.hh
  vent.hh
  vent_set.hh
Source code (src/)
  simple_vent.cc
  vent.cc
  vent_set.cc
Verification (verif/)
  SIM_verif
Validation (validation/)
  None

## Slide 7: Code Review : Coding Standards Compliance
Model is compliant

## Slide 8: Code Review : Architecture Review
Class SimpleVent
  Produces a force/torque pair, or an instantaneous impulse (linear and angular pair)
  Although vents can be instantiated independently, they are not intended to function independently. The main executive methods are restricted to execution from a Vent Set.
  Does not account for mass depletion
Class Vent
  Standard vent; inherits the capabilities of a simple vent and adds mass depletion capabilities.
Class VentSet
  Manager class; the VentSet provides a single access point for a grouping of vents that are to be operated together.
  Provides methods for manipulating all the vents at once, or one at a time.
  Collects forces and impulses from all the vents, combining them to provide a net force and torque pair, or and instantaneous linear and angular impulse pair.
  Inherits from the CML SubscriptionBase class which provides management of the activity status of the model.

## Slide 9: Code Review : Delta Updates
01/19/2023: MR !5678
  Closes Issue #1542 (11/2022): VentSet deactivation wrap-up preferred behavior
  SimpleVent Class:
    Added unset methods for direction, force, force mag, impulse, impulse mag, duration
    Added hold flags, consolidating force-impulse-duration consistency logic
    Added virtual methods for polymorphic extension
  Vent Class:
    Added unset methods for exhaust speed and flowrate
    Added polymorphic stop_venting method to switch vent off
  VentSet Class
    Added time as constructor argument and dyn_time as protected attribute for timed vents
    Added error catch in start_vent/start_vents methods
  Verification clean-up and new tests

## Slide 10: Code Review : Code Coverage
See exceptions in docs Section 5.1

## Slide 11: Initial Project Implementation
Not directly used in SIM_orion
Used in ammonia vent, PSA vent and urine vent models

## Slide 12: Verification: SIM_verif
SIM_verif
  See docs, Chapter 5

## Slide 13: Follow-on Work
ToDOs
  Turner 01/2023 in vent.cc:
    Could make start_venting have an option to support running without mass-flow, like a simple-vent
  Turner 2020/01 in vent_set.hh:
    Investigate use of varargs or variadic templates to support a set of vents each running off its own specified DynMassBody
    Implement a Vent type running off a -DynamicMassString rather than a single tank